GFDex Sortie Brief – B272 – 26 February 2007

Mesoscale Cyclone and Targeted observations of SAP south of Iceland (Plan 44)

Mission Scientists: Ian Renfrew, Nina Petersen, Emma Irvine, Inge Johansson, Haraldur Olafsson, Dave Sproson

Aims

- Map out 3D structure of mesoscale cyclone using a mixture of high-level and low-level legs

- High-level legs at 25-27 kft, straight and level, cutting through cyclone with cross.

- Low-level legs at 2000 ft and 5000 ft, straight and level, to sample wind, temperature, etc

- Dropsonde sampling every 30 nm (30-50 km) within cyclone

- Dropsonde release near Icelandic coast for topographic gravity waves

- Dropsonde releases evenly spaced around SAP for Targeted observation purposes

| GFD44 | Time | Manoeuvre | Distance (nm) | Duration (min) | Total time (min) |
| --- | --- | --- | --- | --- | --- |
| 1 | 0900 | Take off Keflavík , transit to 62N, 19W. | 154 | ~30 | ~30 |
| 2 |  | Straight level run at 25-30 kft, due east to 62N, 11W. Most efficient speed. Dropsonde releases every 30 nm (7 in total) | 225 | ~45 | ~75 |
| 3 |  | High-level leg due south (heading 180o) to 60N, 11W.Dropsonde release here. | 120 | ~25 | ~100 |
| 4 |  | High-level leg due west (heading 270o) to 60N, 15W.Dropsonde release here. | 120 | ~25 | ~125 |
| 5 |  | Straight level run at 25-30 kft, due north to 63N, 15W. From 61.5 N to 63N, Dropsonde releases every 40 nm (3 in total). | 210 | ~50 | ~175 |
| 6 |  | High-level leg to 64.33N, 16W. Dropsonde release here | 56 | ~6 | ~180 |
| 7 |  | Profile descent to 63N, 15W. Fast descent (2000 ft per min?) to 10 kft. Slower descent (1000 ft per min) to 2000 ft. | 56 | ~20 | ~190 |
| 8 |  | Straight low-level leg at 2000 ft to 61N, 15W (heading due south). Science speed | 150 | ~45 | ~245 |
| 9 |  | Climb and head to 60N, 19W. Dropsonde release here | 132 | ~30 | ~275 |
| 10 |  | Transit to Keflavik | 260 | ~35 | ~310 |