GFDex Sortie Brief  – 3rd March 2007 – Greenland lee cyclone

Mission Scientist 1 – G. Nína Petersen

Mission Scientists – Jón Egill Kristjánsson, Haraldur Ólafsson, Melvyn Shapiro, Ivan Føre, Idar Barstad

Aims

- Map out 3-D structure of the deep extra-tropical cyclone located at approximately 61oN 38oW under the influence of NW flow over Greenland

- Low-level flight legs to capture the structure of the back-bent warm front that is wrapped around the low centre

| B275 | Time | Maneuver | Distance (nm) | Duration (min) | Total time (min) |
| --- | --- | --- | --- | --- | --- |
| 1 | 9.30 | Take off from Keflavík, head towards 61o50N 35oW at 25-30 kft, dropping one sonde at midpoint of leg (63o10N 28o20W) | 360 |  |  |
| 2 |  | From 61o50N 35W to 61oN 38oW at 25-30 kft drop sondes every 50 nm (3 sondes) | 100 |  |  |
| 3 |  | High level leg from 61oN 38oW to 60oN 41oW, dropping sondes every 25 nm (4 sondes) | 105 |  |  |
| 4 |  | Straight level leg at 25-30 kft from 60oN 41oW to 61o50N 41oW | 95 |  |  |
| 5 |  | Straight level run at 25-30 kft from 61o50N 41oW to 60o30N 36oW, dropping every 20 nm (8 sondes), including start point | 160 |  |  |
| 6 |  | Profile descent to 5,000ft from 60o30N 36oW back to 61o50N 41oW. | 160 |  |  |
| 7 |  | Straight level run at 5,000 ft from 61o50N 41oW to 60oN 38oW. If not enough fuel, cut this leg any time. | 140 |  |  |
| 8 |  | Straight level run at 5,000 ft from 60oN 38oW to 61o30N 38oW. If not enough fuel, cut this leg any time. | 90 |  |  |
| 9 |  | Transit back to Keflavík | 450 |  |  |