ENV-2E02   ENERGY RESOURCES 2005

Lecture Handout 1

1.  Introduction

2.  History of Electricity Supply

- Generic aspects of the generation of Electricity  common to all forms of resources

- Environmental Impacts of Energy Resources

1. INTRODUCTION

1.1  GENERAL INTRODUCTION

Energy issues are complex and involve an understanding of the following  topics

physical factors

technical factors

economic factors

political factors

social factors

environmental factors

Considerations of Energy  matters which involve only one of these are likely to be flawed and lead to incorrect decisions.

1.2 CONVERSION FACTORS etc.

Quantity of Energy  - basic unit is Joule

(symbol (J =  1 Nm)

|  | 1 Btu (British Thermal Unit) | 1.05506 kJ |
| --- | --- | --- |
|  | 1 Therm | 0.105506 GJ |
|  | 1 calorie | 4.1868 J |
|  | 1 kcal (or Kal) | 4.1868 kJ |
|  | 1 tonne coal equivalent (UK)` | 24 GJ |
|  | 1 tonne coal equivalent (EC) | 29.4 GJ |
|  | 1 tonne oil equivalent | 46 GJ |
|  | 1 barrel of oil | 6.7 GJ |
|  | 1 gallon (UK) oil | 192 MJ |
|  | 1 litre oil | 42 MJ |
|  | 1 tonne peat | 14 GJ |
|  | 1 tonne wood | 15-20 GJ |
|  | 1 cu m gas | 38 MJ |
|  | 1 kWh | 3.6 MJ |
|  | 1 MWh | 3.6 GJ |
|  | 1 GWh | 3.6 TJ |
|  | 1 TWh | 3.6 PJ |

Power:   rate of dissipation of energy

basic unit - Watt (W)  =  1  J s-1

|  | 1 Btu hr-1 | 0.293072 W |
| --- | --- | --- |
|  | 1 kcal hr-1 | 1.1630 W |
|  | 1 horse-power | 0.7457 kW |

NOTE:   You CANNOT convert kWh to kW or MW – they are totally different units.   kWh, MWh implies that a time interval is involved – in this case it is an hour.

If there is a wind turbine rated at 1.5 MW (e.g. Swaffham),  one cannot work out how much energy is generated unless a time interval is used,  and also the LOAD FACTOR- i.e. the proportion of time it actuall is in use.

For wind energy a typical Load Factor is between 28 and 33% (say 30%),  so in a year one might expect the turbine at Swaffham to generate  1.5 * 8760  * 0.3 =  3942 MWh –

[8760 is the number of hour in a year]

Specific Energy   unit kJ kg-1

1 Btu hr-1       =  2.326   kJ kg-1

Mechanical Equivalent of Heat

1 kcal     =       4.1868 kJ

Specific Heat of Water

(i.e. energy required to raise temperature of  1  kg of water through 1 degree Celsius).

1  Btu lb-1 F-1    =  4.1868 kJ kg-1  oC-1

Power per unit area/U - value conversion/conductivity

|  | 1 Btu hr-1 ft-2 | 3.1546 W m-2 |
| --- | --- | --- |
| U-value | 1 Btu hr-1 ft-2 F-1 | 5.678 W m-2 oC-1 |
| conductivity | 1 Btu hr-1 ft-1 F-1 | 1.7307 W m-1 oC-1 |

Efficiency of combustion:-

Domestic

open coal fire            10 - 30%

gas central heating       ~  75%

coal central heating     ~  40%

oil central heating    ~  65 - 70%

gas condensing CH       ~  90%

Industrial

Oil/gas/coal                   85 - 90%

Efficiency of electricity generation and load factors

| generation | typical efficiency | load factor UK |
| --- | --- | --- |
| coal | 35 - 37% | 70% |
| oil | 32-34% | 10-15% |
| gas (CCGT) | 47-53% | 75% |
| Magnox | 25% | 80+% |
| AGR | 39-40% | 85% |
| PWR | 31% | 75% ????? |
| hydro | 80 - 90% | 35% |
| tidal | 80 - 90% | 16 - 20% for barrage ? 30% for turbine |
| Wind | 35 - 40% | 21-29% (Llandinam) typical modern turbine ~ 30% |

S.I.   Symbols - basic units

J    -   Joule

K   -    Kelvin

s    -    second

m  -    metre

kg -   kilogram

Derived S.I. Unit used in energy

N   -   Newton  (basic unit of force)

J   -    Joule - basic unit of Work/Energy

(1 J  =  1 Nm)

W  -    Watt   1 J s-1

# Other Symbols

|  | Btu | British Thermal Unit |
| --- | --- | --- |
|  | C | degree Celsius |
|  | F | degree Fahrenheit |
|  | ft | foot |
|  | hp | horse power |
|  | mtce | million tonnes of coal equivalent |
|  | mtoe (mtep) | million tonnes of oil equivalent (million tonnes equivalent de petrole) |

S.I. prefixes relevant to Energy Options

| m | milli | 10-3 |
| --- | --- | --- |
| k | kilo | 103 |
| M | Mega | 106 |
| G | Giga | 109 |
| T | Tera | 1012 |
| P | Peta | 1015 |
| E | Exa | 1018 |

Total UK consumption of Energy is approximately   10.5 EJ

Total UK electricity consumption = 365 TWh   =  1.31 EJ

1.3.  ENERGY SUPPLY

Prior to 1800 most sources of energy were obtained locally,  although there was an increasing movement of coal.

In modern society,  the source of energy and the point of use are often widely separated.

UK situation - until late 1960's we had no natural gas

# Gas

Until  early 1970's all gas was generated locally

Coal was transported to local gas works for generation, and chemical bi-products were sold.

Coal was thus the national energy vector even though gas was the local vector

# Electricity

The movement away from coal as the national energy vector began with the establishment of the Central Electricity Authority before the war

Since 1980 we have a highly integrated National Grid for the distribution of electricity and a complementary gas network as well as key oil pipe transmission lines.

All such transmission involves loss

electricity   2.5%  on National grid

5%  on Area and local grids

gas and oil both require energy for pumping.

An integrated network will tend to lead towards a centralised system of supply,  although this does not have to be the case.

e.g. coal fired power stations situated mostly on coal fields,  oil fired power stations adjacent to oil refineries etc.

An ideal energy vector would be one which is easily, efficiently, and conveniently transported,  has a high energy density,  and can be readily stored to meet fluctuations in demand.

| Energy Vector | convenience in transport | energy efficiency of transport | storage |
| --- | --- | --- | --- |
| coal | * | *** | **** |
| oil | ** | ** | ***** |
| gas | ** | ** | ** |
| electricity | *** | * | negligible |

# Some Advantages of centralised supply

less over capacity is needed to cover for emergencies as standby capacity can be shared.

larger plant tend to be more efficient

price variation over the country can be minimised

countrywide security is probably higher than for a decentralised system

# Some Disadvantages

transmission is required - hence inevitable loss  (with electricity,  probably more than by transporting coal).

large units are less suitable for energy conservation e.g. CHP

tends to be controlled by few people

no sense of local community "owning its own energy plant"

Centralised systems are a logical development of the use of fossil fuel or nuclear power.

Decentralised systems

will be local and available at point of use

do not require transmission

Some Renewable sources are ideal in this respect.

1.4 Annual Requirement of Fuel to supply UK's Electricity Needs

UK  electricity demand would require approximately

|  | million tonnes coal |
| --- | --- |
|  | million tonnes oil |
|  | billion cubic metres gas |
|  | tonnes of Uranium in conventional reactors |
|  | tonnes of Uranium in Fast Breeder Reactors |
|  | tonnes of Lithium (for conversion to Tritium for D - T fusion) |
|  | tonnes of deuterium in D - D fusion |
|  | Wind Turbines the size of Swaffham |
|  | sq km of solar collector [taking note of UK climate data] |
|  | sq km of land for biomass |

# Transport Requirements for Fuel

Each Coal fired Power Station requires up to 20 train loads  of coal per day (20 000 tonnes) when working on full load.

Currently each reactor in UK requires one delivery of fuel rods every 2 -4 weeks.

A similar quantity of spent fuel rods is sent to Sellafield for reprocessing,  but since the load is very much heavier (50 tonne transport container for every 2 tonnes of spent fuel),  the number of  journeys is more frequent (typically once every 1 - 2 weeks).

1.5 Information about Energy

Material is often presented in a very biased way

DO NOT ACCEPT ANY VALUES  no matter how respected the text without appraising them in a critical and unbiased way – no matter what you view is.

values quoted are often over-estimates or under-estimates

often assumptions made are unrealistic or biased

sometimes one side in the argument has it right! - more often the truth lies between extremes.

Need to critically think about data and values quoted in references and particularly newspapers  and popular press.

Must be able to see flaws in arguments and do simple calculations (if necessary) to check information  before  coming to a rational decision

Your arguments for a particular standpoint which will be much more convincing if you can turn the opponents data to your advantage to prove your case rather than use data which may be challenged by your opponents.

for example:-

if you take an anti-nuclear stance, then if you can use data from the pro-nuclear lobby to prove your case this will be much more convincing than using your own data which the pro-nuclear lobby may say is flawed

conversely

if you can take a pro-nuclear stance using data or assumptions from anti-nuclear lobby it will enhance your case

## Example:-

To replace the equivalent of Sizewell B Power Station,  the land area required would be.

## Pro Nuclear Lobby

around 800 - 900 sq kms    compared to just under 1 sq km for Sizewell

Anti Nuclear Lobby

Area required is only 5%   of  Sizewell.    - implying  0.05 sq km

## WHO IS CORRECT?

Actual area of Sizewell is around  220 acres = 0.9 sq km. and is not in dispute.

1.5.1.  Nuclear Lobby calculation

Sizewell generates 1188 MW at a load factor of 75%

i.e.  equivalent to 891 MW (891000 kW) continuous output

The Swaffham Turbine is rated at 1.5 MW and has a blade diameter of 67m

However,  Wind Turbines have a load factor of 30% (extensive data now available from Llandinam), and an availability of 95%

Mean output per turbine is 1.5*0.3 *0.95 = 427.5kW

So total number of turbines needed = 891000/450

=  2084 turbines

Since turbines must be spaced at 10 blade diameters,

it is possible to get 9 turbines per sq km on a square array or

10.4 on the more compact triangular array.

So area for turbines is  935 sq km for a square array

but   810 sq km for a triangular array

So basic claim by Nuclear Lobby of ~ 800 – 900 sq km is correct.

What is potential flaw in their argument?

1.5.2 Anti Nuclear Calculation

Accept basic premises of Nuclear argument

i.e.    mean load  = 891 000 kW

Load factor of Wind Turbines is 30%,  but would

suggest availability is higher as 98%.     This latter is very little different from 95%, but using the figure gives and effective output of  441 kW   (as opposed to 427.5)

On that basis only     2020 turbines are needed.

However,  the diameter of the supporting tower is about 4m,  so the area of land covered by each wind turbine is

D2/4   =       3.1415926 *  52 /4 per turbine

=   0.039 sq km  in total or

or  4.35% of Sizewell

What is flaw in this argument?

------------------------

Nuclear argument does not recognise that intervening land can be used for a few purposes e.g. Agriculture - but not housing main roads etc.

Anti-nuclear argument does not recognise that actual area of Sizewell includes landscaped areas,  administrative areas,  maintenance areas,  and maintenance access  roads.   Further  it does not allow land area needed for maintenance in wind farm.

1.5.3 Compare like with like

Each Wind Turbine needs  an area of 67 m dia around each turbine on which the ground has been stabilised to take weight of 20+ tonne cranes.  Also tracks for access to each turbine are needed.

So true area around each turbine is just over 1000 sq m,  and the

area of track 2.5m wide (and 670m long for each turbine) would be 1670 sqm

area around each turbine ~ 3525 sqm

So the total area of land unavailable for other purposes per turbine is 5195 sq m or for all turbines is  10.8 sq km

very much less than nuclear lobby

very much more than anti-nuclear lobby

Using the argument advanced by anti-nuclear lobby could thus backfire.

Important to concentrate on issues which are more relevant

e.g.

all land from wind farm could be recovered for normal use readily

but

10%  of area of nuclear power station could not be recovered for at least 100 years

2.  HISTORY OF ELECTRICITY SUPPLY IN UK

2.1   Early Background   1900 - 1957

Prior to 1900 - numerous small utilities sprang up in towns and cities.  Many operated on DC (Direct Current).

In early 20th Century,  Local Authorities generally took control of supply.  Supply was switched to AC,  but some areas still had DC until after Second World War.

Switch to AC was for several reasons,  but there are many disadvantages.  With the technology available today it is probably unlikely that we would have gone to AC.

In 1924 there were about 435 power stations supplying electricity.

In 1930s,  the Central Electricity Board was set up and this began establishing a National Grid,  initially at 33kV,  then 66 kV and finally by the early 1950's,  132 kV.

Higher voltages for transmission minimise transmission losses.

power  =      volts   x     amps

and   loss      =      resistance x   (amps)2

The CEB started building larger stations connected to grid, and these displaced older stations as they came for renewal.  At end of War,  the number of stations had dropped to 345.

cf     240  in 1965

168  in 1976

78  in 1986

1947  Electricity Act  (effectively Nationalisation)  included statement that " Electricity must be generated as efficiently as possible"  This (or the interpretation of this statement) hindered progress to a more effective system of supply.

In most other countries,  supply of electricity, gas etc. remained in the control of the Local Authority.

The Act also set up the BRITISH ELECTRICITY AUTHORITY  as the successor company to the CEB.

Finally in mid 1950's,  the BRITISH ELECTRICITY AUTHORITY was reorganised as follows:-

CEGB   -      responsible for generation and supply to the local  Electricity Boards.   Apart from a few customers  e.g.  British Rail, British Steel,  the CEGB did not  supply electricity to customers.  The CEGB only  operated in England and WALES,  and was  divided into 5 regions.    The CEGB operated nuclear, coal, oil, gas, and hydro stations.

ELECTRICITY BOARDS -  These purchased electricity from  the CEGB and distributed it to customers.  There   were 12 Area Boards (e.g.  MANWEB,   SEEBOARD etc).  These Boards did not generate electricity.

ELECTRICITY COUNCIL -  This was a body covering the  whole Electricity Industry,  and had a Research   Centre at Capenhurst.

IN SCOTLAND,  the organisation was different.

SOUTH OF SCOTLAND ELECTRICITY BOARD.

This  generated and supplied electricity to customers in  the  South of Scotland.   It also operated nuclear power stations.

NORTH OF SCOTLAND HYDRO BOARD.

This initially  generated electricity mostly by Hydro-electricity and supplied electricity to the North of Scotland  and  the outlying islands.  Fossil Fired power   stations were built, and the hydro component   became less than 50%.

The NSHB exchanged electricity with SSEB who in turn  exchanged electricity with the CEGB.

A low power link was also installed to link the CEGB with  Electricite de France (EdF).

2.2   DEVELOPMENTS ELECTRICITY SUPPLY   1957-90

CEGB began installing Super-grid at voltages of 275 kV and finally 400 kV.

Decision taken in early 1960's to build new power stations to avoid shortages of late 1950's and early 1960's.  These were sited on coal fields or on coast (Nuclear and Oil).   Remoteness was a factor for nuclear,  but proximity of Oil Refineries was factor for Oil  e.g.  Pembroke Dock  adjacent to Milford Haven,  or Fawley (next to Esso)  or Ince (next to Shell) etc.  Essentially with the majority of coal in the north this meant that we would ship electricity around the Country rather than move coal to power stations in general locality where power was needed.

Consequences:-

Less coal by rail             -  closure of lines in 1960's?

More Grid Lines needed

( even today there are parts of the  country which are vulnerable  eg    SW and SE).

Made implementation of CHP difficult.

Power stations became very  large as smokeless zones in cities became implemented. Large stations  did not have nearby heat sink for CHP.

2.3 HISTORICAL DATA on ELECTRICITY GENERATION

| YEAR | UNITS (GWh) | Capacity (MW) | Max Demand (MW) | Efficiency (%) | YEAR | UNITS (GWh) | Capacity (MW) | Max Demand (MW) | Efficiency (%) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1930 |  |  |  | 17.93 | 1975 | 252359 | 69452 | 46677 |  |
| 1946 | 35509 |  |  | 22.00 | 1976 | 255879 | 69747 | 47902 |  |
| 1947 |  |  |  |  | 1977 | 262007 | 69911 | 48605 | 33.16 |
| 1948 |  |  |  |  | 1978 | 267299 | 71426 | 50144 |  |
| 1949 |  |  |  |  | 1979 | 278736 | 70886 | 49582 |  |
| 1950 |  |  |  |  | 1980 | 264862 | 68382 | 48284 |  |
| 1951 |  |  |  |  | 1981 | 258743 | 68106 | 49187 |  |
| 1952 |  |  |  |  | 1982 | 253328 | 67022 | 47333 |  |
| 1953 |  |  |  |  | 1983 | 255854 | 68632 | 47414 |  |
| 1954 |  |  |  |  | 1984 | 261534 | 69763 | 51710 |  |
| 1955 | 89093 | 22489 |  |  | 1985 | 274427 | 69787 | 50943 |  |
| 1956 | 95767 | 24615 |  |  | 1986 | 282754 | 70055 | 53980 |  |
| 1957 | 99967 | 26635 | ~20000 | 26.17 | 1987 | 291331 | 69637 | 52495 | 35.08 |
| 1958 | 107337 | 28023 |  |  | 1988 | 297884 | 74557 | 52229 | 35.47 |
| 1959 | 114748 | 30015 |  |  | 1989 | 291751 | 74557 | 53414 | * |
| 1960 | 129846 | 31865 | 26918 |  | 1990 | 297461 | 73518 | 54068 | * |
| 1961 | 138274 | 33922 |  |  | 1991 | 300540 | 70528 | 54472 | * |
| 1962 | 151641 | 37207 |  |  | 1992 | 298469 | 67499 | 51663 | * |
| 1963 | 163432 | 39289 |  |  | 1993 | 301793 | 69117 | 54848 | * |
| 1964 | 171567 | 39974 |  |  | 1994 | 305850 | 68988 | 52362 | * |
| 1965 | 183716 | 43941 |  |  | 1995 | 314780 | 70128 | 55611 | 36.0** |
| 1966 | 189655 | 46233 |  |  | 1996 | 327209 | 73172 | 56815 | 36.9** |
| 1967 | 195244 | 50031 | ~39000 | 28.89 | 1997 | 329471 | 72696 | 56965 | 36.7** |
| 1968 | 207656 | 53559 |  |  | 1998 | 342699 | 73380 | 56312 | 36.5** |
| 1969 | 221491 | 60538 | 43027 |  | 1999 | 347670 | 75446 | 57849 | 36.8** |
| 1970 | 230687 | 65567 | 43270 |  | 2000 | 357266 | 78451 | 58452 |  |
| 1971 | 237233 | 68794 | 44914 |  | 2001 | 364174 | 79678 | 58589 |  |
| 1972 | 244466 | 71125 | 45868 |  | 2002 | 366871 | 76991 | 61717 |  |
| 1973 | 261819 | 72136 | 44883 |  | 2003 | 377836 | 78524 | 60501 |  |
| 1974 | 253301 | 71816 | 46526 |  | 2004 |  |  |  |  |

*   Since Privatisation there have been no detailed records (which are accessible) kept of efficiency of individual power stations

** Efficiency Data for 1995 - 2003 refers only to conventional non-nuclear steam stations for compatibility with earlier data

2.4 Ordering of Power Stations pre- privatisation:-

In the early 1960's there was a massive ordering of power stations,  mostly coal-fired,  but as oil became cheap,  more and more oil stations were ordered,  and the "Oil Burn" increased to about 26%.

In 1970-1973,  all new stations ordered were oil,  and some were still under construction  8-9 years after oil crisis.

From a position of under - capacity in early 1960's,  to one of

adequate capacity around 1970,  the CEGB was faced with a massive over-capacity in mid 1970's as growth in electricity stagnated.

Two stations only ordered (mostly on grounds other than supply - e.g. unemployment etc.)  -   DRAX completion and Heysham II nuclear station.

In early 1980's  CEGB mothballed some plant,  but accelerated closure of others.

From over-estimating demand  (a trend which was apparent throughout 1970's),  they now under-estimated growth in demand.  Indeed their central assumption for Sizewell Inquiry proved a gross under-estimate,  and electricity demand grew at a rate approaching their high-growth scenario.

DANGER by mid 1980's that there would be a short fall in capacity by mid 1990's as stations were getting progressively older and not being replaced.

- Electricity Act:-  Made CHP more likely.  Also made it

easier for private generation of electricity.

1986  -   SIZEWELL ordered  - on line in 1994

proposals for West Burton B and Fawley B - both

coal fired.  Both turned down on "Environmental

Grounds".

1988   Proposals for Privatisation - England and Wales

2.5   Privatisation    - 1990 -

2.5.1 Generation:-

Initially  Big  G  (thenNational Power)  to include    nuclear - later the nuclear side

was separated as Nuclear Electric (Government Owned)

Little G  (now PowerGen)

But private companies/ Area Boards could also  generate.

POOL began operation on 1st April 1990

In 1996    Nuclear Electric   was split  into British Energy (privatised) and Magnox Electric.

# From 1996 - 2000

Increased Number of Independents

Deregulation of Supply to all consumers

National Power and PowerGen required to sell some of their plant - mostly bouight by Eastern Energy

National Grid sold interest in Pumped STorage to First Hydro - later Mission Edison who have now als purchased other fossil fuelled pwoer plant e.g. Fiddler's Ferry.

BNFL  took over Magnox Electric in 1997.

In 2000 Ntaional Power demerged into INNOGY which took over most of UK business and International Power - which now devotes its effort mostly to overseas issues.

Increased Number of Independents

Deregulation of Supply to all consumers

Renewables Obligation Document Published for Consultation

New Electricity Trading Arrangements began on  27th March 2001

- Renewables Obligation came into force on 1st April 2002.

- Several problems have emerged in last 18 months as price of wholesale electricity has been forced down.  Examples – problems at AES (DRAX),  then British Energy,  then TXU (which had three generating stations),  and even PowerGen were not immune as they mothballed a gas fired station which was only around 8 years old.

2.5.2 Distribution:-

National Grid Company took over main distribution, but also have control of Pumped Storage Schemes.

Supply:-     Local Area Boards (or Regional Electricity

Company (REC))-  similar to pre-

privatisation but with increased powers.

Large consumers (i.e. over 1MW) can purchase electricity from ANY AREA BOARD.   To be reduced to 100kW in 1995

and restriction removed altogether in 1998/9

- In recent years there have been many take-overs/mergers in the Supply section of the Industry – e.g.  TXU taking over Eastern,  then in Autumn 2002 PowerGen took over TXU.

- Companies like PowerGen were soley involved in generation until mid 1990s.  Now they are also major players in supply sector.

2.5.3 SCOTLAND

SSEB and NSHB were privatised largely as they existed (apart from Nuclear component) - i.e. the cover everything from generation to supply.

Scotland generates about 50% electricity from Nuclear.

2.5.4 OTHER POINTS:-

- Introduction of non-fossil fuel obligation  (NFFO - details later)- to subsidise non-fossil fuels.  Initially  a single level was set to include nuclear and renewables.  Later there were separate targets for nuclear and renewables.  Finally,  there were separate targets for the different renewables.

- For NFFO-1 and NFFO-2 this subsidy was phased out in 1998.

- NFFO-3 and SRO (Scottish renewables order was announced in January 1995).

- NFFO 4 and NFF05 followed in 1997 and 1999.

- Subsidy for NFFO-3, 4, 5 continues to run for 20 years after start.

- Renewable Obligation replaces NFFO

2.5.5 GENERATION BY GAS

Until the late 1980's,  generation of electricity from gas was uncompetitive as the prices charge for electricity generation were TWICE those for other uses.  This was partly a result of EC Legislation which was subsequently relaxed.

The legacy of no power station building (apart from Sizewell) for a decade meant that new station were urgently needed.

The UK had no Combined Cycle Gas Turbines in 1991 (apart from a very small demonstration unit 76 MW).

Numerous proposals for CCGTs have been made and currently  13815MW (Jan 1st 1998) have been completed, with a further 5000MW + under construction.

One small fluidized bed combustion plant has also been commissioned (80MW) compared to 2000 MW for a typical coal station.

Construction of Power Stations is now in hands of private companies, and most new proposals are NOT from National Power or PowerGen.  In the past,  CEGB made estimates 7 years in advance and order stations accordingly.

3.    GENERATION OF ELECTRICITY

3.1   Introduction

Electricity is generated whenever there is movement of a conducting material within a magnetic field.

Frequently the conducting material is a loop (or series of loops of copper wire) which is rotated within the poles of a powerful magnet.

Generation may be either as AC - alternating Current

or DC - direct current.

As we shall see later  A.C. has traditionally been better for centralised systems and  are likely to continue to be so UNLESS  super-conductivity becomes a reality.

Renewable Energy sources are much more suited to  a DC system,  but in most instances they have to conform to AC systems

In power generation,  the coil is mounted on a rotor which revolves at 3000 rpm (50 Hz in Europe) or 3600 rpm (60 Hz in North America).  The magnet is usually an electro magnet on the stator.

The motive force for rotating the coil may be provided by any convenient mechanical means (e.g. a water turbine,  wind turbine or by the expansion of steam in a steam turbine.

The generator is typically 95% efficient,  losses arising from friction,  air-resistance,  and heating in the copper wires.  Cooling is usually done using hydrogen as despite its fire risk,  it is the most efficient "dry coolant"

Electricity is also used in the generator to power the electro-magnet.  This is usually generated separately in the Exciter which is like a small generator,  but this time a permanent magnet is used because the power to be generated is relatively small.

3.2  The Turbine

The motive power to turn the generator comes from the turbine.

In hydro stations,  either a jet of water may be directed at a series of cups or specially shaped blades are used to extract energy

In wind power,  turbines normally use lift forces on specially shaped blades for higher efficiency in electricity generation - older machines used for mechanical pumping have many blades and operated by drag forces

In steam turbines (nuclear, fossil fuel, biomass, waste,  geothermal),  high pressure steam is directed at a series of blades causing them to turn.  The outlet steam is then redirected via fixed blades onto further moveable blades.  In a modern power station there may be over 30 sets of moveable and fixed blades.

3.3  Electric Power - 	A QUICK REVISION

Electric power is measured in Watts and is simply obtained by multiplying the voltage by the current.

thus     power   =     volts  x   amps

In the UK,  the voltage is 240 at the moment,  so an electric kettle consuming 3 kW will draw   3000 / 240  =  12.5 amps

(hence the reason why we have 13 amp plugs)

In the USA where the voltage is 120,  the current drawn would be 25 amps.

Since the size of the cables increases with the likely current,  the thickness of wire in all electrical circuits in North America will be larger than in the UK.

Alternatively, of course,  if the same current is drawn,  then the power will be less,  and the kettle will take longer to boil.

3.4 Synchronism

Almost all electricity in generated as ALTERNATING CURRENT in which both the voltage and current follow a sine curve - see Fig. 3.1.  In Europe,  the oscillation is 50 Hz (50 cycles per second).

Fig. 3.1   Variation in voltage in the UK domestic supply.  The cycle frequency is 50 Hz.

Suppose an additional generator comes on line.  It must be in EXACT SYNCHRONISM (or phase) with all the other generators otherwise it could oppose the electricity generated elsewhere.

ALL GENERATORS IN THE UK ARE RUNNING AT PRECISELY THE SAME SPEED AND ARE IN PHASE WITH ONE ANOTHER.

3.5  Reactive Appliances

If AC. is passed through a resistance such as an electric fire,  power is dissipated as given in section 3.3.     In such appliances,  both the current and the voltage are in phase.

However,  many appliances are REACTIVE (e.g. electric motors,  fluorescent light tubes etc.).    In these cases,  the current (I) and the voltage (V) are NOT in phase (see Fig. 3.2) ,  and the useful power consumed will be:-

where  is the phase difference between the current and voltage.

If the current and voltage are in phase,   = 0 and all the power supplied is useful power.

cos  is known as the power factor and may be 0.8 or lower.

Fig.  3.2 Effect of a reactive load is to cause a phase shift between voltage and current.

Thus the useful power (measured in kilowatts) may be 20% less than the power supplied (measured in kilovars).

Some appliances cause the current to lead the voltage,  for others the reverse is true.  With careful management it is possible to apply POWER FACTOR CORRECTION to improve the utilisation of energy.

3.6.  ELECTRICITY SUPPLY

All utilities supply power as A.C.  (although this was not always the case).

D.C. (direct current)   does not generally suffer from the above problems (except as transients).

Renewable Energy Sources are more suited to D.C. and there is thus a technical bias against the Renewables.

D.C. is used for some transmission lines but requires inversion and rectification at each end of line.

D.C. transmission becomes economic for long  (> 500 km) overhead lines (e.g. Canada,  USA,  Scandinavia)

D.C. transmission becomes economic for underground cables for relatively short lengths (~30 km).

A reason why link to FRANCE is DC is that the phase of the UK supply is generally different from that in Europe

3.7 ADVANTAGES OF AC and DC.

3.7.1 ADVANTAGES of AC

almost all appliances run of AC.

voltages can be readily transformed from one voltage to another.

[This is important in transmission as the power lost in transmission is equal to  I2 R  (where R is the resistance of the wire).  For a given amount of power,  the current may be reduced by increasing the voltage in the same proportion]

Thus a single QUAD 400 kV circuit can carry 1000 MW.

but  power = volts x amps

so current flowing is  1000 x 106 /400 000   =  2500 amps

if voltage were only 100 kV,  the current would be 10000 amps, and the loss in transmission would be 16 times as great.

3.7.2 DISADVANTAGES OF AC.

all generators must be in synchronism

separate transmission networks cannot be interconnected directly unless both systems are in exact synchronism

power carried though an overhead line is lower than for DC.

power carried through an underground cable can be significantly lower than for DC.

reactive power losses can cause significant waste of electricity.

3.7.3 ADVANTAGES OR DC.

no problems with synchronism (ideal for renewable sources)

separate transmission networks can be interconnected (provided voltage is compatible)

can be used to interconnect separate AC. networks

greater power can be transmitted through both overhead and underground cables

reactive power loads cause little difficulty except when switched on or off.

3.7.4 DISADVANTAGES OF DC.

voltages cannot be changed except with costly invertors (which temporarily convert DC. into a quasi AC)

few appliance run on DC.

Most early electricity supplies used DC,  but decision to switch to AC. was a close thing,  and mainly hinged on ability to transform voltages as large power inverters/ rectifiers were unavailable at the time.

If decision were made now,  the reverse decision may well have been made.

IF super conductivity at ambient temperature becomes a reality,  then the whole question of transmission may well be reviewed.

??   DC.  would be used for UHV transmission and inverted to AC. for local transmission/use.

Ultimately end users may be given supply in DC. with local inverters to run older AC. appliances

3.8 THREE PHASE

Electricity in the domestic market is usually as single phase A.C.  Three wires are connected to most appliances.

one wire is the local earth (there is an earthing point in each house,  and all metal pipe work must also be connected to this earthing).

one wire is the NEUTRAL (NOT NEGATIVE!!!!) line

one wire is the LINE voltage (NOT LIVE!!!!)

The voltage oscillates at 50 Hz from +340 volts to - 340 volts as a sine wave  (Fig. 3.3)

Fig. 3.3   The normal electricity supply in the UK has a voltage which varies between +340 and - 340.   The root mean square (RMS) is 240.

The ROOT MEAN SQUARE  is 240 volts and this is the figure which is normally used as it is the effective voltage.

In theory the voltage of the neutral line should be zero and should not differ from earth potential.  In reality,  there is always a small varying voltage on the NEUTRAL LINE.

Using a SINGLE PHASE supply means that two wires must connect the consumer to the generator.

This is satisfactory for resistive loads (like electric fires),  but does not give the most effective power for motors as there can be only two 'kicks' to the motor for each revolution.

For large consumers,  a three-phase supply is provided,  where the phase angle of phase 1 is zero, that of phase 2 is 120o, and that of phase 3 is 240o.

If a three phases supply is connected to a motor,  then it will received six 'kicks' per revolution and will thus run more smoothly and efficiently.

If the current consumed on each of the three phases is the same,  there will be no flow in the neutral lines,  and these can be dispensed with entirely.  This obviously leads to a significant saving in the number of cables needed (from 6 to 3).

In the domestic market,  one third of the houses are connected to the RED phase,  one third to the BLUE phase,  and one third to the YELLOW phase

Corresponding to the 240 (RMS) volts of single phase,  the equivalent three phase (RMS) volts between adjacent phases is 415 volts.

The supergrid transmission lines typically have two circuits each of three wires representing the three phases.  An additional cable is usually strung along the top of pylons to mitigate against lightning strikes.

Each wire of each circuit may consists of a bundle of up to 4 separate cables (Think why this should be - have a look on the field course as we pass National Grid Pylons).

In the UK,  six different voltages are used as transmission lines:-

a)  400 kV - National SuperGrid - the largest towers

b)  275 kV - National SuperGrid

c)  132 kV - a few National Super Grid, but mostly   these belong to REC's

d)    66 kV )  the smallest pylons:  owned by REC's

e)    33 kV )

f)     11 kV    owned by REC's - the supports are   usually timber poles.

4.  Environmental Impacts of Energy Resources

| Energy Source | Environmental Issues |
| --- | --- |
| Coal | Mining: Open cast - landscape, ecology, river pollution from tailings, release of radon gas Deep mining: settlement problems, methane, disease amongst miners etc. Spoil heaps Use: SO2 emissions; NOx radioactivity (~30 ManSievert cumulative for UK population per EJ). Flyash, solid ash. Large amount of CO2 - significantly worse than gas, oil or biomass Resource base: centuries Comments: FGD reduce SO2 by 90% - also reduces gaseous radioactive emissions, but increases liquid radioactive waste NOx can be reduced by 60% using new burner types Proposals to freeze CO2 but that would require and increase in power stations by ~30+% New technologies include IGCC, (? MHD). But likely to be 10 - 20 years before they are on stream at least. Even with these the CO2 emissions will still be higher than for gas. |
| Gas | Extraction and transmission: some loss of methane a potent greenhouse gas (~1%+) Use: CO2 but 40-60% that of coal depending on technology NOx increased over coal unless special burners are fitted Low radioactive emission (from radon) Resource base: decades |
| Oil | Extraction and transmission: oil spills causing local ecological disasters Processing: Discharge of chemicals to environment Use: CO2 (intermediate between gas and coal), SO2 can be high if orimulsion is used and NOx Radioactive emission (about same as nuclear but lower than coal) Use for transport: NOx, lead, Benzenes, ozone etc. emitted at low level causing respiratory diseases etc. Resource base: decades |
| Nuclear Power - Nuclear Fission | Uranium mining: Require massive amount of earth movement if using older technologies. Newer methods use pumping of water which causes less problems, but can leak into water courses. Spoil for solid mining also presents a problem Fuel Fabrication: Requires energy for enrichment (slight radioactive emissions ~1-1.5 ManSieverts per Exajoule). Use: Slight radioactive emission in normal operation (3-10 ManSieverts per EJ) Possibility of serious accident in reactors with positive void coefficient: remote possibility of serious accident in reactors with negative void coefficient, but likelihood is dependent on reactor type |

4.  Environmental Impacts of Energy Resources  continued

| Nuclear Power Nuclear Fission – contd. | Reprocessing Effluent discharges are radioactive, but generally less than emissions in normal operation - typically 8 ManSieverts per EJ, [although this was not always so ]- SIXEP has reduced effluent discharges at Sellafield by a factor of 500, and radioactive discharges will be reduced further over the next 5 years. Waste Disposal: Depends onpproach adopted: a) reprocess reduces HLW but increases ILW and LLW b) higher component of HLW and more difficult to encapsulate Long term storage may present problems Decommissioning [controversy over correct approach] Resource Base: decades can be extended to centuries using Fast Breeder Reactors, but this introduces new problems (e.g. pure Plutonium) |
| --- | --- |
| Nuclear Fusion | Potentially a vast source of energy with no toxic waste products (apart from reactors themselves): commercial plants unlikely to be available before 2020 and may be later |
|  | RENEWABLES |
| Solar Thermal | Land use: US estimates give about 1 m2 per GJ per annum collected - hence large areas required for High temperature applications including steam raising for electricity generation (e.g. Bairstow California). In UK all low temperature space heating requirements will require about ~40+m2 for an average house in UK Material: Substantial quantities of steel, copper, fibre glass, glass, and aluminium are used in construction of solar panels, and these all have high energy requirements (typically first 2+ years of running is needed to pay back energy invested in construction). Attendant environmental problems associated with production of these primary materials including chemical discharges etc. Material use is significantly more per unit of energy than conventional technologies but less than wave or OTEC Use: Discharges of chemical used in circuits for anti-freeze, anti-bacteria fluids etc. problems of overheating (even fire) if allowance is not made for excess energy problem in summer. Health Problems: Danger to human/animal eyesight in centralised focusing systems, toxicity of transfer fluids in centralised schemes. Legionnaires Disease could be come more widespread with large scale use of 'direct' solar water heaters. |
| Solar Voltaic | Manufacture: Large quantities of gases many of which are highly toxic are used in manufacture of thin film photo-voltaic cells. Some are flammable, e.g. hydrogen, methane, others warrant concern (e.g. arsine, phosphine, H2S etc., and can be a serious hazard to workforce, and may lead to releases to the environment. Use: Photovoltaic cells generate electricity directly (without being switched on), and the hazard from electric shocks is significantly increased over other methods of electricity generation. |

4.  Environmental Impacts of Energy Resources  continued

| Wind | Use: Visual impact including unsightly tracks for maintenance, noise, television interference, interference with communications, bird strikes, physical injury from blade failures (7% of original blades in California Wind farms failed or showed signs of fatigue), ice formation on blades causing uneven running leading to premature failure, ice thrown off blades. Problems of distraction to drivers etc near main roads, “flashing” sun through blades of turbines on horizon can be serious. |
| --- | --- |
| Geothermal | Use: Airborne Emissions (particularly H2S which is highly toxic) causing ecological changes, chemical and thermal pollution of rivers and surrounding land from spent geothermal fluid, induced seismicity, noise, visual intrusion of escaping steam from numerous wells, ground subsidence (e.g. 3m over 65 sq km area at Wairakei, New Zealand), need to continually drill new wells even in “renewable” locations because of deposition in pipes etc (2% replacement rate per annum in New Zealand needed to maintain resource), conflict with uses by indigenous population which is affecting tourism (Rotorua, New Zealand). |
| Hydro | Construction: Large quantities of materials are needed in large hydro electric schemes. Large dams affect river regime - leading to siltation and down-stream erosion. Loss of habitat, increased soil erosion, change of salinity in some circumstances can have drastic effect on ecology. Displacement of population (China is displacing 1 million people in one scheme alone (see New Scientist Jan 1995 - see also problems on Danube and several other countries). Chemical changes can occur in ground water affecting nutrient balance or increasing toxicity as submerged organic matter decays. Weight of dam and impounded water can induce seismicity. Use: Large impounded lake can be breeding ground for insects - hence disease (upper Volta scheme). Visual impact when water level in reservoir is low can be extensive. In some cases transport communications may be improved, in others they will not. Catastrophic failure of large dams leading to large loss of life (e.g. Malplasset, Vaiont, Teton etc.) |
| Wave | Construction: Mooring problems for offshore devices - foundation problems for devices sitting on sea bed Durability in hostile environment - has to be over designed to withstand extreme storm force conditions Use: Hazard to shipping Reduces waves hitting shore hence coastal erosion ecosystem will be changed to lower energy environment Synchronism problems more acute than wind for offshore devices. Most of UK high energy waves are remote from centres of population - hence additional power lines needed Onshore developments (e.g. Islay) are easier to develop, but resource is greatly reduced. Would be ideal using hydrogen as the energy vector Maintenance of offshore devices would be a problem |

4.  Environmental Impacts of Energy Resources  continued

| Tidal | Construction: Large quantities of materials are needed for the enclosure barrages. Use: Tidal regimes are affected, siltation can limit life of project severely. Barrier poses obstruction to shipping and marine life. Ground water levels will change as will the mean salinity thus affecting the ecological balance. Effluent discharges from the surrounding land will not disperse as tidal range is reduced. Some species of birds may thrive, but many will lose their habitat. Increased resource for recreation. Alternative could make use of existing man-made causeways – e.g. Churchill Barriers in Orkney: difference in tide times of several hours. |
| --- | --- |
| Marine Current | Construction: Design presents challenge – large horizontal thrusts Foundation problems Use: Under water devices pose a threat to shipping Under water maintenance Can be constructed as modules – thus less environmentally damaging than conventional enclosure tidal schemes. Operates like a wind turbine, but needs less materials as water is nearly 1000 times as dense as air Could extract energy offshore |
| Biomass | Land Use: Significant areas of land are required for energy crops, and some authorities question whether energy crops are in fact net producers of energy in view of significant quantities of fossil fuels used for machinery for transport etc.. Use: Energy Crops can be harvested and “burnt” or transformed into other fuels (e.g. “ethanol” a petrol substitute). There are emissions including CO2, although in sustainable use, this is neutral on the overall CO2 balance. Reduced SO2 but increased NOx can be expected from plant. Other emissions can include aromatic compounds such as benzene which are carcinogenic. Areas of crops need to be cleared and this can have a temporary visual impact, but such changes can lead to adverse changes in soil erosion characteristics and also soil chemistry and biology. Managed crops would reduce likelihood of fire damage to forests, but climate and ground water flow may be affected. |
| Waste | Sources: Sewage, Landfill, Refuse Sewage from human and animal waste can be digested to generate methane, but significant quantities of the methane are needed to keep the process up to temperature. Landfill causes releases of methane (a potent greenhouse gas), and burning this although generating CO2 reduces the effective greenhouse impact. Other waste may be collected and burnt to generate heat, processed to develop refuse derived fuel or used to generate electricity. There are numerous processes available, but some of the key environmental concerns are: Release of dioxins and other toxins from incorrect combustion of waste products. Emission of carbon monoxide, NOx, HCl, SO2 etc, the exact proportions depend on the nature of the waste. HCl is in higher concentrations than the combustion of coal, SO2 should be less than for coal while there is disagreement as to whether NOx emissions are greater for waste than for coal. There is a visual impact of the plant and an associated smell, but there is also a benefit in that less landfill space is required with its own attendant problems. |

4.  Environmental Impacts of Energy Resources  continued

## Limits to Exploitation  - No stars – no limitation – more stars = greater restriction

| Resource |  | Technical | Economic | Environmental | Planning/ Social Acceptance |
| --- | --- | --- | --- | --- | --- |
| Coal | Conventional |  | * | **** | *** |
|  | FBC | * | * | ** | * |
|  | IGCC | ** | * | ** | ** |
| Oil |  |  | * | **** | * |
| Gas |  |  |  |  |  |
| Fission | Thermal |  | ? | - normal | ? |
|  |  |  |  | ** disposal | ? |
|  | FBR | *** | ? | * normal | ? |
|  |  |  |  | ** disposal | ? |
| Fusion |  | **** | ** | * | ? |
| Solar | Hot Water |  | **** |  |  |
|  | Central | *** | *** |  | ? |
|  | Photovoltaic | ** | *** | * |  |
| Wind | Onshore |  | * | *? | **??? |
|  | Offshore | ** | *** | ? | ? |
| Geothermal | Steam |  |  | ** | ? |
|  | Hot aquifers |  | *** | ? | ? |
|  | HDR | *** | *** | * (seismisity ?) | ? |
|  | Other | ***** | ***** | ? | ? |
| Hydro | Large Scale |  |  | *? | ** |
|  | Small Scale | * | ** |  |  |
| Wave | Shore based | * | ** | ? | ? |
|  | Off shore | **** | *** | ? | ? |
| Tidal | Barrage |  | * | *? |  |
|  | Marine currents | *** | *** | ? |  |
| Waste |  |  |  | * | ** |
| Biomass | Direct |  | * | ? | * |
|  | gasification | ** | ** | ? | * |
|  | Energy Crops | ** | ** | ? | * |

# Text boxes

Space for additional notes

Space for additional notes