GFDex Sortie Brief – 21st February 2007 – Reverse Tip Jet (Flight plan 13)

Mission Scientist 1 – Ian Renfrew

Mission Scientists – Kent Moore, Nina Petersen, Carling Hay, Stephen Outten, Tadayasu Oghiushi

Aims

- Map out 3D structure of reverse tip jet using high-level and low-level legs

- Map out near-surface winds and associated air-sea turbulent fluxes

- High-level legs between 15-25 kft, straight and level, generally perpendicular to jet axis

- Dropsonde sampling every 20-25 nm (30-40 km)

| GFD13 | Time | Manoeuvre | Distance (nm) | Duration (min) | Total time (min) |
| --- | --- | --- | --- | --- | --- |
| 1 | 10.30 | Take off Keflavík, transit to 62N, 40W | 490 | ~90 | ~90 |
| 2 |  | Straight level run at 20-25 kft, from 62N, 40W to 62N, 42W, perpendicular to jet axis. Science speed. Dropsondes every 20 nm (4 in total). | 56 | ~15 | 105 |
| 3 |  | Straight level run at 20-25 kft From 62N 42W to 61.5N, 41W. | 41 | ~12 | 117 |
| 4 |  | Straight level run at 20-25 kft, from 61.5N, 41W to 60.2N, 41.5W. Science speed Dropsondes every 25 nm (4 in total) | 80 | ~25 | 142 |
| 5 |  | Straight level run at 20-25 kft, from 60.2N, 41.5W to 60N, 43W | 46 | ~13 | 155 |
| 6 |  | Straight level run at 20-25 kft, from 60N, 43W to 59.5N, 41W, perpendicular to jet axis. Science speed. Dropsondes every 20 nm (4 in total). | 67 | ~23 | 178 |
| 7 |  | Rapid descent to ~10,000 ft, profile descent to minimum safe altitude |  | ~5 | 183 |
| 8 |  | Straight low-level leg at MSA, from 59.5N, 41W towards coast, parallel to dropsonde leg (heading ~300deg). If poor visibility ~59.7N,42W | 33 | ~10 | 193 |
| 9 |  | Straight low-level leg at MSA north at 42W to 62.2N, 42W | 30 | ~10 | 203 |
| 10 |  | Straight low-level leg at MSA parallel to leg 8 (~heading 120). | 32 | ~10 | 213 |
| 11 |  | Climb and transit to Keflavik | ~570 | ~100 | 313 |